AERIAL LIFTS

SAFE WORK PRACTICES

- Only trained and authorized workers are permitted to operate aerial lifts.

- Complete the Daily Aerial Lift inspection prior to first using the lift.

- Report any deficiencies or problems concerning the lift.

- Do not use a damaged lift.

- Always maintain and operate aerial lifts according to the manufacturer's instructions.

- Never override hydraulic, mechanical, or electrical safety devices.

- Do not allow workers to position themselves between overhead hazards, such as joists and beams, and the rails of the basket. Movement of the lift could crush the worker(s).

- Maintain a minimum clearance of at least 10 feet away from the nearest energized overhead lines.

- Always treat power lines, wires and other conductors as energized, even if they are down or appear to be insulated.

- Use a fully body harness with a lanyard attached to the approved anchor point. Do not “tie-off” to the side rails.

- Set the brakes and use wheel chocks when on an incline.

- Use outriggers, if provided.

- Do not exceed the load limits of the equipment. Allow for the combined weight of the worker, tools and materials.

AERIAL LIFT DAILY INSPECTION

Per IPS’s safety procedures and the OSHA regulations aerial lifts – both JLG’s (articulating boom) and scissor lifts required daily written inspections prior to use. These inspections include both an operational control usage and visual inspection for leaks and damage.

The inspection must include: Lift controls; tires, body and guard rails; hydraulic compounds (leakage); brakes; all manufactured safety alarms and lights, including back up alarms and the work area and planned route.

Also - rental units are “pre-inspected” by the supplier upon delivery.

Any aerial lifts which do not pass the daily inspection or fail while being used shall be reported to the foreman, tagged “Out of Service”, the keys pulled until repaired.

(Use IPS Aerial Lift Inspection Form #8 – and report any damage)

Please contact Safety for additional information or assistance.

SAFETY MEETING SIGN-OFF SHEET

TOPIC OF MEETING: 	AERIAL LIFT SAFETY

SAFETY MEETING SERIES 22-2018

FOREMAN:

LOCATION/ JOB NUMBER:

| NAME (print) | SS# (last four) | TRADE | SIGNATURE |
| --- | --- | --- | --- |
| 1. |  |  |  |
| 2. |  |  |  |
| 3. |  |  |  |
| 4. |  |  |  |
| 5. |  |  |  |
| 6. |  |  |  |
| 7. |  |  |  |
| 8. |  |  |  |
| 9. |  |  |  |
| 10. |  |  |  |
| 11. |  |  |  |
| 12. |  |  |  |
| 13. |  |  |  |
| 14. |  |  |  |
| 15. |  |  |  |
| 16. |  |  |  |
| 17. |  |  |  |
| 18. |  |  |  |